NCTS-RPB2 80mm Mini Portable Thermal Receipt Printer

Products Features：

●Business style design, more fashion

●Support 1.D,2.D bar code printing

●While compatible with Windows, Linux, Android and IOS systems

●With 2500mAh rechargeable lithium polymer battery, super battery lasting time, with smart power 		 saving and power consumption control functions, to ensure longer print time

●Support USB, COM, Bluetooth,Wi-Fi ,USB+Bluetooth(V2.0),USB+Bluetooth(V3.0+V4.0)

●Special power remaining indicator light, to control the printer power at any time

●Support sound and light reminder when lack of paper or printing abnormal

●Anti fall of 1.5M cement floor

Application:

Warehousing, transportation, logistics, supermarket, tobacco, hydropower reading, mobile government affairs, mobile police, postal and other industries

Parameters：

| Item | Parameter |
| --- | --- |
| Print parameter | Printing Method | Thermal Line |
|  | Effective Printing Width | 72mm |
|  | Resolution | 576 dots/line（8dots/mm，203dpi） |
|  | Priting Speed | 90mm/S |
|  | Interface | USB (standard USB2.0 communication protocol, support Windows, Linux, Android, IOS) Bluetooth (Bluetooth2.0, Bluetooth3.0+4.0,support Android, IOS) WIFI (2.4GHZ, ATA, AP, ATA+AP mode) |
|  | Line spacing | 3.75mm（Can adjust line spacing by command） |
|  | Line No. | Font A:48 character /Line Font B:64 character/Line Simple, traditional Chinese-24 lines |
|  | Character | The standard GB18030 simplified / traditional Chinese characters library |
|  | Character Size | ANK character，Font A：1.5×3.0mm（12×24 dots） Font B：1.1×2.1mm（9×17 dots） Simplified/Traditional：3.0×3.0mm(24×24dots） |
| Bar code character | Extended character set | PC437/Katakana/PC850/PC860/PC863/PC865/WestEurope/Greek/Hebrew/EastEurope/Iran/WPC1252/PC866/PC852/PC858/IranII/Latvian/Arabic/PT151,1251/PC737/WPC/1257/ThaiVietnam/PC864/PC1001/(Latvian)/(PC1001)/(PT151,1251)/(WPC1257)/(PC864)/(Vietnam)/(Thai) |
|  | Bar code | 1D.Bar code：UPC-A/UPC-E/JAN13(EAN13)/JAN8(EAN8)CODE39/ITF/ CODABAR/CODE93/CODE128 2D.Bar code：QRCODE |
| Graphics printing | Graphics printing | Supports bitmap download and print |
| Power saving Mode | Smart power saving | Support |
|  | Variable speed printing | Support |
|  | Consumption | Support |
|  | Dormancy | Support |
|  | Sensor | Lack of paper detection |
| Indicator | Power Display | Support |
|  | Charge Indicator | Support |
|  | Lack of paper | Support |
|  | Beep | Lack of paper, printing abnormal alarm |
| Paper | Type | Thermal |
|  | Width | 79.5±0.5mm |
|  | thickness | ≤0.12mm |
|  | Diameter | ≤40mm |
|  | Feed | Easy（Clamshell feed） |
| Print commands | Commands | ESC/POS |
| Power | Type | Rechargeable Lithium polymer battery |
|  | Capacity | 2500mAh/7.4V, can be charged more than 800 times sustainable printing 150 meters or 4 hours under normal use |
|  | Charger | 9.0V/2A |
| Buffer | Input | 4KB |
|  | NV Flash | 40KB |
| Physical features | Weight | 285G |
|  | Dimension | 114*103*50(MM) |
| Environment | Operating | Temp：5 ~ 45℃， Humidity：10 ~ 80% |
|  | Storage | Temp：-10 ~ 50℃ ，Humidity：10 ~ 90%（No Dew） |
| Reliability | Print head life | 50KM（Printing Density≤12.5） |
| Software | Driver | Android,IOS,Linux,,WinXP,Win7,Win8,Win8.1,Win10 |